## Slide 1: Linz-Donawitz Process (for SS316, at 98% Purity)
Robinson Bui, Karen Izaguirre, Ezra Ju, Logan Kuhn, Esther Marroquin, Grace Wang

## Slide 2: Background & Relevance

## Slide 3: Linz-Donawitz (LD) Process History
Originated in Switzerland 1940's
Named after the first two towns it was first used in
Also known as: basic oxygen process
Linz
Donawitz

## Slide 4
(1856) First inexpensive steelmaking process
(1949) LD Process discovery
Henry Bessemer
Robert Durrer
But before that?
Notes: - wasn’t used
- Main difference between Bessemer process and ld air vs oxygen, why ld was not possible and efficient until high purity oxygen became available and affordable in large quant
- But for the product of our process…

## Slide 5: Steel History: in General
Evidence of steel tool use (Iberian Peninsula)
800 BCE
Wootz steel (India & Sri Lanka)
300 BCE
Steel tips for weapons Song Dynasty (China)
1000 CE
Notes: Some examples…
Recent studies University of Freiburg: Iberian peninsula, stelae on rocks that could only be chiseled by steel
Wootz steel later used as lauching point for Damascus steel
Song Dynasty in 1000 CE waterwheels superheating molten ore, relevant as china is now where the majority of desired product is made
What steel is our desired product…

## Slide 6: Stainless Steel SS316
Composition:
Cr (16-18%) Si (≤ 0.75%)
Ni (10-14%) C (≤0.08%)
Mo (2-3%) P (≤ 0.045%)
Mn (≤ 2%) S (≤ 0.03%)
Heat resistance
Corrosion Resistance
Durability
Notes: If interested the typical percent compositions below % comps
Will resist under continuous 425-860°C
- talk abt
Chemical & Pharmaceutical Industry: Used in chemical tanks, processing equipment, and piping due to its resistance to corrosive chemicals.
Marine Applications: Ideal for shipbuilding, offshore platforms, and coastal structures because of its ability to withstand salty environments.
Medical Industry: Found in surgical instruments and implants due to its biocompatibility and resistance to body fluids.
Food & Beverage Industry: Used in processing equipment, storage tanks, and kitchen appliances for its hygienic properties.
Automotive & Aerospace: Components like exhaust systems and aircraft fittings benefit from its heat resistance and durability.

## Slide 7: Reaction Process
The entire process of producing SS316 starts with another process involving coke, iron ore, and a blast furnace.
We’re focusing on the step after this, where the resultant pig iron is placed into a basic oxygen furnace.
Wright, R. N. (2016). Chapter 14 - Relevant Aspects of Carbon and Low-Alloy Steel Metallurgy. In Wire Technology (Second Edition, pp. 201–233). essay, Butterworth-Heinemann. Retrieved October 19, 2025, from https://www.sciencedirect.com/science/article/pii/B9780128026502000145 .

## Slide 8: Problem Statement
Produce 1000kg of SS316
Recycle Ratio: 3:1
Reacts in a basic oxygen furnace with pure oxygen at 8-12 bar with a lance
Furnace reaches 1700°C and is jacketed with molten salt
Heat of Reaction -27.89 MJ/kg SS316 (reaction is exothermic)
Pig Iron Composition | 
Alloy | % Comp.
Carbon | 4.05%
Silicon | 0.5%
Phosphorus | 0.05%
Iron | 94.56%
Sulfur | 0.04%
Manganese | 0.8%
SS316 Composition | 
Alloy | % Comp.
Carbon | 0.07%
Chromium | 17%
Nickel | 11%
Molybdenum | 2%
Iron | 70%

## Slide 9: Assumptions
We assume our FPC is 85%
Assume all reaction intermediates go to completion
We derived it to make our system match the given recycle ratio of 3
Our calculations are not all inclusive – we solved several different versions of the system
We want excess O2 and limiting CaO
Our reaction is exothermic, but because we must melt iron to 1700°C, the overall process is endothermic

## Slide 10: Mass Balance

## Slide 11: Chemical Equations
Steel Production
Impurity Oxidation
**Impurity Equations Are Exothermic

## Slide 12: Composition of Pig Iron Impurities During Reaction
Goswami, P. (2025, January 12). LD converter process in steelmaking ► MetaTechX. MetaTechX. https://metatechx.in/ld-converter-process-in-steelmaking
Species | %comp before | %compafter | Ratio
C | 4.00 | 0.1 | 0.025
S | 0.046 | 0.025 | 0.543
Si | 0.9 | 0 | 0
Mn | 1.00 | 0.12 | 0.12
P | 0.07 | 0.017 | 0.243
Notes: We calculated the first pass conversion of each impurity using this chart. Values on the chart were eyeballed and worked with

## Slide 13: Recycle Ratio
 |  |  | Material Mass (g) | 
Species | Rxn. Eff. | 1-Eff | Reacted | Unreacted
O2: | 85.00% | 15.00% | 48.1210243 | 8.491945469
C: | 85.00% | 15.00% | 0.69833096 | 0.123234875
Cr: | 85.00% | 15.00% | 179.258031 | 31.63377014
Ni: | 85.00% | 15.00% | 107.241091 | 18.9248985
Mo: | 85.00% | 15.00% | 20.6840451 | 3.650125612
Fe: | 85.00% | 15.00% | 692.118502 | 122.1385591
CaO: | 85.00% | 15.00% | 1.05607881 | 0.186366849
 |  | Total: | 1049.1771 | 177.7108475
 | Stream Variables Mass (g) |  |  | 
RR: | 0.160978291 | %comp | Mass (1k kg) | Mass (g)
Charge Stream: |  | 100.00% | 1103.94293 | 1103.943
 | Pig Iron Charge: | 66.30% | 731.93581 | 731.9358
 | Lime Charge: | 0.10% | 1.05607881 | 1.056079
 | Chromium Charge: | 16.37% | 180.758325 | 180.7583
 | Nickel Charge: | 10.23% | 112.885359 | 112.8854
 | Molybdenum Charge: | 1.87% | 20.6943923 | 20.69439
 | Oxygen Charge: | 5.13% | 56.6129698 | 56.61297
Reactor Outlet: |  |  |  | 
SS316 Product Outlet: |  |  | 1000 | 1000
Slag Product Outlet: |  |  |  | 17.80716
Recycled Stream: |  |  | 177.710847 | 177.7108
Net Flow Rate: |  |  | 1281.65378 | 1281.654
Net Flow Rate Check: |  |  |  | 1281.654

## Slide 14
Notes: What are these curves?

## Slide 15: Reagent Breakdown
17% Chromium
11% Nickel
2% Molybdenum
70% Iron
0.07% Carbon
Example of Desired Product SS136
C: 4.05% S: 0.04%
Si: 0.5% Mn: 0.8%
P: 0.05%
Fe: 94.56%
Pig Iron Composition
Mo: 99.95%
Chromium Purity
Ni: 95%
Nickel Purity
Molybdenum Purity
Cr: 99.17%

## Slide 16
Basic Oxygen Furnace
Separator
Pig Iron Stream
C: 4.05%
S: 0.04%
Si: 0.5%
Mn: 0.8%
P: 0.05%
Ti: 0.00%
Fe: 95.0%
Stream 1
CaO: 100%
Cr: 99.17%
Ni 95%
Mo 99.95
Inert
Stream 3
Reactants
Steel
Slag
Gases
Inert
Product Stream (SS136)
Fe: 70%
Cr: 17.92%
Ni: 11%
Mo: 2%
C: 0.07%
Purge Stream
CO Slag
Inert O2
Recycle Stream
Recycle Ratio: 3:1
Block Flow Diagram
Recycle Stream
Impure Iron, Ni, Cr, Mo,
Notes: Am leaving this to Logan / Ezra; Aspen and/or by hand calculations

## Slide 17: Stream Compositions
Charge Stream Composition |  |  | %comp by mass |  | 
 |  | Mass (g) |  |  | Mass (g)
Pig Iron Stream | %comp | 66.30% | Cr Stream | %comp | 16.37%
C: | 4.05% | 29.6434 | Cr: | 99.17% | 179.2580308
Si: | 0.50% | 3.659679 | Inerts: | 0.83% | 1.500294097
P: | 0.05% | 0.365968 | Total: | 100.00% | 180.7583249
Fe: | 94.56% | 692.1185 | Ni Stream | %comp | 10.23%
S: | 0.04% | 0.292774 | Ni: | 95.00% | 107.2410915
Mn: | 0.80% | 5.855486 | Inerts: | 5.00% | 5.644267973
Ti: | 0.00% | 0 | Total: | 100.00% | 112.8853595
Inerts: | 0.00% | 0 | Mo Stream | %comp | 1.87%
Total: | 100.00% | 731.9358 | Mo: | 99.95% | 20.68404514
Lime Stream: | %comp | 0.10% | Inerts: | 0.05% | 0.010347196
CaO: | 100% | 1.056079 | Total: | 100.00% | 20.69439233
O2: | 100% | 56.61297 |  |  | 
Reactor Recycled Stream: |  | 
Species | %comp | Mass (g)
C: | 0.069% | 0.123234875
Si: | 0.000% | 0
P: | 0.055% | 0.098529942
Fe: | 68.729% | 122.1385591
S: | 0.099% | 0.176396315
Mn: | 0.438% | 0.778966126
Cr: | 17.801% | 31.63377014
Ni: | 10.649% | 18.9248985
Mo: | 2.054% | 3.650125612
CaO: | 0.105% | 0.186366849
Total: | 100.000% | 177.7108475
Total: | 100.000% | 
SS316 Template: |  | 
Species | Mass (g) | %comp
C: | 0.7 | 0.07%
Cr: | 170 | 17.00%
Ni: | 110 | 11.00%
Mo: | 20 | 2.00%
Fe: | 699.3 | 69.93%
Total: | 1000 | 100.00%
Reactor Outlet Stream Composition |  |  |  | 
Fe(total): | 814.2571 |  |  | 
Unreacted Reagents |  |  |  | 
1st-pass% (of %comp): |  | %comp | %corrected | Mass (g)
C: | 2.50% | 0.101% | 0.101% | 0.821565836
Si: | 0.00% | 0.000% | 0.000% | 0
P: | 24.29% | 0.012% | 0.012% | 0.098529942
S: | 54.35% | 0.022% | 0.022% | 0.176396315
Mn: | 12.00% | 0.096% | 0.095% | 0.778966126
Fe(total): | 106.12% | 100.35% | 99.770% | 814.2570607
Total: | N/A | 100.58% | 100.000% | 816.1325189
 |  |  | Material Mass (g) | 
Species | Rxn. Eff. | 1-Eff | Reacted | Unreacted
O2: | 85.00% | 15.00% | 48.1210243 | 8.491945469
C: | 85.00% | 15.00% | 0.69833096 | 0.123234875
Cr: | 85.00% | 15.00% | 179.258031 | 31.63377014
Ni: | 85.00% | 15.00% | 107.241091 | 18.9248985
Mo: | 85.00% | 15.00% | 20.6840451 | 3.650125612
Fe: | 85.00% | 15.00% | 692.118502 | 122.1385591
CaO: | 85.00% | 15.00% | 1.05607881 | 0.186366849
 |  | Total: | 1049.1771 | 177.7108475
Slag Product (g): |  |  | SS316 Tot. Similarity: | 
 | 20.79534 |  |  | 99.01%
Purge Stream (g): |  |  | SS316 Tot. Mass (g): | 
 | 83.1476 |  |  | 1000

## Slide 18
The Real Block Flow Diagram

## Slide 19: Energy Balance

## Slide 20
Basic Oxygen Furnace
Separator
Pig Iron Stream
C: 4.05%
S: 0.04%
Si: 0.5%
Mn: 0.8%
P: 0.05%
Ti: 0.00%
Fe: 95.0%
Stream 1
CaO: 100%
Cr: 99.17%
Ni 95%
Mo 99.95
Inert
Stream 3
Reactants
Steel
Slag
Gases
Inert
Product Stream (SS136)
Fe: 70%
Cr: 17.92%
Ni: 11%
Mo: 2%
C: 0.07%
Purge Stream
CO Slag
Inert O2
Recycle Stream
Recycle Ratio: 3:1
Block Flow Diagram
Recycle Stream
Impure Iron, Ni, Cr, Mo,
25°C, 1atm
??? °C
1700°C
1700°C
1700°C
1700°C
Notes: Am leaving this to Logan / Ezra; Aspen and/or by hand calculations

## Slide 21: Assumptions
Fresh Feed at STP
No atmospheric change
0.16 RR; 85% FPC
Inert material is insignificant
No heat loss in transportation
Things that can melt, will melt

## Slide 22: Energy Balance
Energy Balance Equation

## Slide 23: Energy Balance
No kinetic energy
No potential energy
No shaft work
0
0
0

## Slide 24: Energy Balance
Specific Heat
Heat of Reaction
Inlet stream NOT at STP

## Slide 25: Energy Balance
Specific Heat values
Equation NIST uses
Values found from NIST WebBook & other tables

## Slide 26: Energy Balance
NIST WebBook values
Steel values are from Office of Scientific and Technical Information (OSTI)
From 25°C – 1700°C

## Slide 27: Energy Balance
Iron’s values don’t seem correct…
Temp Range (K) | H (kJ/mol)
298-700 | 12.000
700-1042 | -13533.218
1042-1100 | -7119.913
1100-1700 | -559.057
Sum: | -21200.188
Temp Range (K) | H (kJ/mol)
0-1184 | 26.960
1184-1665 | 33.619
1665-1700 | 52.621
Sum: | 113.2
NIST WebBook Iron
JANAF-NIST Iron
Notes: Point this out briefly

## Slide 28: Energy Balance
Inlet stream at STP… almost
Values from NIST WebBook

## Slide 29: Energy Balance
Inlet stream NOT at STP
Values from NIST WebBook
Heat of fusion was not accounted for

## Slide 30
Basic Oxygen Furnace
Separator
Pig Iron Stream
C: 4.05%
S: 0.04%
Si: 0.5%
Mn: 0.8%
P: 0.05%
Ti: 0.00%
Fe: 95.0%
Stream 1
CaO: 100%
Cr: 99.17%
Ni 95%
Mo 99.95
Inert
Stream 3
Reactants
Steel
Slag
Gases
Inert
Product Stream (SS136)
Fe: 70%
Cr: 17.92%
Ni: 11%
Mo: 2%
C: 0.07%
Purge Stream
CO Slag
Inert O2
Recycle Stream
Recycle Ratio: 3:1
Block Flow Diagram
Recycle Stream
Impure Iron, Ni, Cr, Mo,
25°C, 1atm
51 °C
1700°C
1700°C
1700°C
1700°C
Notes: Am leaving this to Logan / Ezra; Aspen and/or by hand calculations

## Slide 31: Energy Balance
Things melt!
NIST breaks up values

## Slide 32: Energy Balance
Calculate outlet stream from 51°C to 1700°C
237,715.567 kJ/kg SS316

## Slide 33: Energy Balance
Heat of reaction
Products – reactants
Extent of reaction calculated using FPY
NIST WebBook
Used the FPC to calculate moles reacted
-27,892.619 kJ/kg SS316

## Slide 34: Energy Balance
Scale it up!
Endothermic
A higher recycle ratio will yield a lower value
Scale up to 1000 kg/day

## Slide 35: Atom & Process Economy

## Slide 36: Atom Economy Calculations
Total Mass - 90.82%
Species | Mass | Mol. Mass | Moles
Pig Iron: | 731.9358096 | 15.1194157 | 15.1194157
Lime: | 1.056078811 | 56.077 | 0.018832655
Cr: | 180.7583249 | 51.996 | 3.476389048
Ni: | 112.8853595 | 58.693 | 1.923318956
Mo: | 20.69439233 | 95.95 | 0.21567892
O2: | 56.61296979 | 31.998 | 1.769265885
Total: | 1103.942935 | 49.01424231 | 22.52290116
Notes: It doesn’t make sense for us to have an atom economy because the reactions are only purifying the already created iron. We are also making an alloy which is just mixing. Like think about trail mix
Atom economy tells us how efficiently the atoms from our reactants end up in the final SS316 product. We start with pig iron, oxygen, lime, and pure alloying metals. But not all of those atoms make it into the steel—many go into slag or off-gas when impurities like Si, Mn, P, S, and carbon are removed.
Because steelmaking requires oxidation and impurity removal, a large fraction of atoms must leave the system, which inherently lowers atom economy. So AE gives us the theoretical chemical efficiency of the process, independent of cost or real operational losses.

## Slide 37: Process Economy Calculations
Profit (yearly): $38,665.89
Species | Price (USD) | Per Unit | Per Unit (g) | Mass Req | Cost | Upscaled | Upsc./year
Pig Iron: | $300.00 | ton | $0.0003000 | 731.93581 | $0.22 | $219.58 | $80,146.97
Lime: | $20.00 | ton | $0.0000200 | 1.05607881 | $0.00 | $0.02 | $7.71
Cr: | $10.00 | kg | $0.0100000 | 180.758325 | $1.81 | $1,807.58 | $659,767.89
Ni: | $20.00 | kg | $0.0200000 | 112.885359 | $2.26 | $2,257.71 | $824,063.12
Mo: | $78.00 | kg | $0.0780000 | 20.6943923 | $1.61 | $1,614.16 | $589,169.35
O2: | $0.00 | g | $0.0000000 | 56.6129698 | $0.00 | $0.00 | $0.00
Totals: |  |  | $0.1083200 |  | $5.90 | $5,899.05 | $2,153,155.04
Products: |  |  |  | Produced | Revenue |  | $0.00
SS316: | $6,000.00 | ton | $0.0060000 | 1000 | $6.00 | $6,000.00 | $2,190,000.00
Slag: | $60.00 | ton | $0.0000600 | 83.1475951 | $0.00 | $4.99 | $1,820.93
Totals: |  |  | $0.0060600 |  | $6.00 | $6,004.99 | $2,191,820.93
Notes: Process economy looks at real industrial efficiency—how much of our input materials and costs are converted into sellable SS316. It includes everything atom economy does not: slag generation, purge losses, alloy costs, oxygen use, and the recycle ratio.
Here, SS316 is the main revenue stream, while slag has minimal value. PE tells us how profitable and efficient the actual BOF and alloying process is, rather than how efficient it is on paper.
But because of our location we are able to sell the slag to neighboring places so we are also able to make a profit from it. Which we will go over in a bit.

## Slide 38: Real Life Applications

## Slide 39: Location
Coega SEZ, South Africa
Low cost for alloys and pig iron
High selling price of SS316
Port city; can export easily
Economic incentives in SEZs
Proximity to potential clients
Notes: Lower costs for raw materials
  South Africa is the 7th largest producer of iron ore
High selling price of SS316
Location we have chosen: Port Elizabeth and Port of Nqgura
  Trade to China, US, Germany
Special Economic Zone: designated area with different economic policies to support targeted economic activities and draw in investors
  Reduced corporate income tax, building allowances, tax reliefs on employment, customs controlled area, pre-existing services and infrastructure
Potential Clients
  Cemza: cement to sell slag
  Hella marine: miritime lighting and electronics that must withstand saltwater

## Slide 40: Ideal Profit
Scaling the Process economy up from small scale:
Costs Analysis |  |  |  |  |  |  | 
Species | Price (USD) | Per Unit | Per Unit (g) | Mass Req | Cost | Upscaled | Upsc./year
Pig Iron: | $250.00 | ton | $0.0002500 | 731.93581 | $0.18 | $182.98 | $66,789.14
Lime: | $20.00 | ton | $0.0000200 | 1.05607881 | $0.00 | $0.02 | $7.71
Cr: | $5.00 | kg | $0.0050000 | 180.758325 | $0.90 | $903.79 | $329,883.94
Ni: | $10.00 | kg | $0.0100000 | 112.885359 | $1.13 | $1,128.85 | $412,031.56
Mo: | $55.00 | kg | $0.0550000 | 20.6943923 | $1.14 | $1,138.19 | $415,439.93
O2: | $0.00 | g | $0.0000000 | 56.6129698 | $0.00 | $0.00 | $0.00
Totals: |  |  | $0.0702700 |  | $3.35 | $3,353.84 | $1,224,152.28
Products: |  |  |  | Produced | Revenue |  | $0.00
SS316: | $6,000.00 | ton | $0.0060000 | 1000 | $6.00 | $6,000.00 | $2,190,000.00
Slag: | $60.00 | ton | $0.0000600 | 83.1475951 | $0.00 | $4.99 | $1,820.93
Totals: |  |  | $0.0060600 |  | $6.00 | $6,004.99 | $2,191,820.93
Upsale: | 1000 kg/day | 
Conversions: |  | 
Ton ->Kg-> Grams |  | 
1 | 1000 | 1000000
Profit (yearly): $967,668.65
Notes: Process economy = actual products on Alibaba
Here = general prices of raw materials in South Africa
Ideal profit = increased profit, can sell steel as lost as $3500

## Slide 41: Thank You

## Slide 42: References
Asia for Educators, C. U. (n.d.). China in 1000 CE. Song Dynasty China | Asia for Educators. https://afe.easia.columbia.edu/songdynasty-module/econ-rev-iron-steel.html (slide 5)
AMC. (2025, Mar 5). What is stainless steel 316? uses, grades, and composition. Amardeep Steel Centre. https://www.amardeepsteel.com/blog/what-is-stainless-steel-316-uses-grades-and-composition.html (slide 39)
Benefits of operating within special economic zones (2025). investSA. https://www.investsa.gov.za/special-economic-zones/ (slide 39)
Cemza cement products (2025). Cemza Engineered Cement. https://cemza.co/cement-products/ (slide 39)
Henry Bessemer | Biography, inventions, & facts | britannica. (n.d.-a). https://www.britannica.com/biography/Henry-Bessemer (slide 4)
Iron ore production in south africa and major projects (2024, Aug 23). Mining Technology. https://www.mining-technology.com/data-insights/iron-ore-in-south-africa/?cf-view (slide 39)
Kadezabek, S. (2025, June 11). History of steel: Ancient invention to modern innovations. Service Steel Warehouse. https://www.servicesteel.org/resources/history-of-steel (slide 5)
Materials processing | definition, examples, types, & facts | britannica. (n.d.-c). https://www.britannica.com/technology/materials-processing (slide 3)
Maximizing efficiency and safety in pharmaceutical research and manufacturing with Stainless Steel. The Stainless Steel Solution: Enhancing Pharmaceutical Manufacturing and Research Safety. (n.d.). https://www.unifiedalloys.com/blog/stainless-steel-benefits-pharma (slide 6)
Metallurgy - iron, steel, alloy | britannica. (n.d.-d). https://www.britannica.com/science/metallurgy/Ferrous-metals (slide 4)
Metals, A. (2023, July 18). Why 316 stainless steel is optimal for Food Processing Equipment. Alliant Metals Inc. https://alliantmetals.com/316-stainless-steel-the-optimum-choice-food-processing/ (slide 6)
SEZ investments (2025). COEGA. https://www.coega.co.za/site/sez-investments (slide 39)
South africa exports by country (2025). https://tradingeconomics.com/south-africa/exports-by-country (slide 39)
Srinivasan, S. (n.d.). Wootz Steel: An Advanced Material of the Ancient World. Wootz Steel: An advanced material of the Ancient World. https://dtrinkle.matse.illinois.edu/MatSE584/articles/wootz_advanced_material/wootz_steel.html (slide 5)
Stainless steel use in marine applications. Stainless Steel Use in Marine Application - Unified Alloys. (n.d.). https://www.unifiedalloys.com/blog/stainless-steel-marine-applications (slide 6)
Stone-working and the earliest steel in Iberia: Scientific analyses and experimental replications of Final bronze age stelae and tools - sciencedirect. (n.d.-e). https://www.sciencedirect.com/science/article/abs/pii/S0305440323000201 (slide 5)
What is stainless steel 316?: Uses, grades, and composition. What is Stainless Steel 316?: Uses, Grades, and Composition. (n.d.). https://www.amardeepsteel.com/blog/what-is-stainless-steel-316-uses-grades-and-composition.html (slide 6)
Wikimedia Foundation. (2025a, April 18). Robert Durrer. Wikipedia. https://en.wikipedia.org/wiki/Robert_Durrer (slide 4)
Wikimedia Foundation. (2025b, October 27). Wootz Steel. Wikipedia. https://en.wikipedia.org/wiki/Wootz_steel (slide 5)
WorldAtlas. (2021, February 25). Austria Maps & Facts. https://www.worldatlas.com/maps/austria (slide 3)